## Slide 1: Medium Access Control Sublayer Chapter 4
  Channel Allocation Problem
  Multiple Access Protocols
  Ethernet
  Wireless LANs
  Broadband Wireless
  Bluetooth
  RFID
  Data Link Layer Switching
Revised: August 2011
Notes: Gray units can be optionally omitted without causing later gaps

## Slide 2: The MAC Sublayer
Responsible for deciding who sends next on a multi-access link
  An important part of the link layer, especially for LANs
Physical
Link
Network
Transport
Application
MAC is in here!

## Slide 3: Channel Allocation Problem (1)
For fixed channel and traffic from N users
  Divide up bandwidth using FDM, TDM, CDMA, etc.
  This is a static allocation, e.g., FM radio
This static allocation performs poorly for bursty traffic
  Allocation to a user will sometimes go unused

## Slide 4: Channel Allocation Problem (2)
Dynamic allocation gives the channel to a user when they need it. Potentially N times as efficient for N users.
Schemes vary with assumptions:
Assumption | Implication
Independent traffic | Often not a good model, but permits analysis
Single channel | No external way to coordinate senders
Observable collisions | Needed for reliability; mechanisms vary
Continuous or slotted time | Slotting may improve performance
Carrier sense | Can improve performance if available

## Slide 5: Multiple Access Protocols
  ALOHA »
  CSMA (Carrier Sense Multiple Access) »
  Collision-free protocols »
  Limited-contention protocols »
  Wireless LAN protocols »

## Slide 6: ALOHA (1)
In pure ALOHA, users transmit frames whenever they have data; users retry after a random time for collisions
  Efficient and low-delay under low load
`
Collision
Collision
Time
User
A
B
C
D
E

## Slide 7: ALOHA (2)
Collisions happen when other users transmit during a vulnerable period that is twice the frame time
  Synchronizing senders to slots can reduce collisions

## Slide 8: ALOHA (3)
Slotted ALOHA is twice as efficient as pure ALOHA
  Low load wastes slots, high loads causes collisions
  Efficiency up to 1/e (37%) for random traffic models

## Slide 9: CSMA (1)
CSMA improves on ALOHA by sensing the channel!
  User doesn’t send if it senses someone else
Variations on what to do if the channel is busy:
  1-persistent (greedy) sends as soon as idle
  Nonpersistent waits a random time then tries again
  p-persistent sends with probability p when idle
Notes: 802.11 uses a refinement of p-persistent CSMA

## Slide 10: CSMA (2) – Persistence
CSMA outperforms ALOHA, and being less persistent is better under high load

## Slide 11: CSMA (3) – Collision Detection
CSMA/CD improvement is to detect/abort collisions
  Reduced contention times improve performance
Collision time is much shorter than frame time

## Slide 12: Collision-Free (1) – Bitmap
Collision-free protocols avoid collisions entirely
  Senders must know when it is their turn to send
The basic bit-map protocol:
  Sender set a bit in contention slot if they have data
  Senders send in turn; everyone knows who has data

## Slide 13: Collision-Free (2) – Token Ring
Token sent round ring defines the sending order
  Station with token may send a frame before passing
  Idea can be used without ring too, e.g., token bus
Station
Direction of
transmission
Token

## Slide 14: Collision-Free (3) – Countdown
Binary countdown improves on the bitmap protocol
  Stations send their address in contention slot (log N bits instead of N bits)
  Medium ORs bits; stations give up when they send a “0” but see a “1”
  Station that sees its full address is next to send

## Slide 15: Limited-Contention Protocols (1)
Idea is to divide stations into groups within which only a very small number are likely to want to send
  Avoids wastage due to idle periods and collisions
Already too many contenders for a good chance of one winner

## Slide 16: Limited Contention (2) –Adaptive Tree Walk
Tree divides stations into groups (nodes) to poll
  Depth first search under nodes with poll collisions
  Start search at lower levels if >1 station expected
Level 0
Level 1
Level 2

## Slide 17: Wireless LAN Protocols (1)
Wireless has complications compared to wired.
Nodes may have different coverage regions
  Leads to hidden and exposed terminals
Nodes can’t detect collisions, i.e., sense while sending
  Makes collisions expensive and to be avoided

## Slide 18: Wireless LANs (2) – Hidden terminals
Hidden terminals are senders that cannot sense each other but nonetheless collide at intended receiver
  Want to prevent; loss of efficiency
  A and C are hidden terminals when sending to B
Hidden = can’t hear each other

## Slide 19: Wireless LANs (3) – Exposed terminals
Exposed terminals are senders who can sense each other but still transmit safely (to different receivers)
  Concurrency desirably; improves performance
  B  A and C  D are exposed terminals
B and C are exposed (to each other)

## Slide 20: Wireless LANs (4) – MACA
MACA protocol grants access for A to send to B:
  A sends RTS to B [left]; B replies with CTS [right]
  A can send with exposed but no hidden terminals
  A sends RTS to B; C and E hear and defer for CTS
  B replies with CTS; D and E hear and defer for data
Notes: This protocol solves the issue of expensive collisions too, since the RTS/CTS are short packets – if there is a collision it will be brief, not as long as a data frame.

## Slide 21: Wireless LANs (4) – MACA
MACA protocol grants access for A to send to B:
  A sends RTS to B [left]; B replies with CTS [right]
  A can send with exposed but no hidden terminals
  A sends RTS to B; C and E hear and defer for CTS
  B replies with CTS; D and E hear and defer for data
Range of D’s transmitter
If D transmitted, it would interfere with A’s transmission to B
Range of E’s transmitter
  E and D are hidden terminals when sending to B
  B and A are exposed while A C and B  D
Notes: This protocol solves the issue of expensive collisions too, since the RTS/CTS are short packets – if there is a collision it will be brief, not as long as a data frame.

## Slide 22: Ethernet
  Classic Ethernet »
  Switched/Fast Ethernet »
  Gigabit/10 Gigabit Ethernet »

## Slide 23: Classic Ethernet (1) – Physical Layer
One shared coaxial cable (bus) to which all hosts attach
  Up to 10 Mbps, with Manchester encoding
  Hosts ran the classic Ethernet protocol for access
The transceiver senses the medium (busy/idle/collision?) and reads and writes bits to it.
This function is now part of the NIC.
bus

## Slide 24: Classic Ethernet (2) – MAC
MAC protocol is 1-persistent CSMA/CD (greedy)
  Random delay (backoff) after collision is computed with BEB (Binary Exponential Backoff)
  Frame format is still used with modern Ethernet
Ethernet
(DIX)
IEEE 802.3
Minimum frame size = 64 bytes, maximum = 1,518 bytes
Notes: 1-persistent (greedy) means sends as soon as idle

## Slide 25: Classic Ethernet (3) – MAC
Collisions can occur and take as long as 2 to detect
   is the time it takes to propagate over the Ethernet
  Leads to minimum packet size for reliable detection

## Slide 26: Classic Ethernet (4) – Performance
Efficient for large frames, even with many senders
  Degrades for small frames (and long LANs)
10 Mbps Ethernet,
64 byte min. frame

## Slide 27: Switched/Fast Ethernet (1)
  Hubs wire all lines into a single star-wired CSMA/CD domain
  Switches isolate each port to a separate domain
    Much greater throughput for multiple ports
    No need for CSMA/CD when using full-duplex lines
Hub is a logical bus which repeats (copies) any bits it sees on one port to all of the other ports
Logical bus

## Slide 28: Switched/Fast Ethernet (2)
Switches can be wired to computers, hubs and switches
  Hubs concentrate traffic from computers
  More on how to switch frames in 4.8
Switch
Twisted pair
Switch ports
Hub

## Slide 29: Switched/Fast Ethernet (3)
Fast Ethernet extended Ethernet from 10 to 100 Mbps
  Twisted pair (with Cat 5) dominated the market
100Base-TX uses two of the four wire pairs in the cable, i.e., one pair of conductors in each direction for full duplex

## Slide 30: Gigabit / 10 Gigabit Ethernet (1)
Switched Gigabit Ethernet is now the garden variety
  With full-duplex lines between computers/switches

## Slide 31: Gigabit / 10 Gigabit Ethernet (1)
  Gigabit Ethernet is commonly run over twisted pair
  10 Gigabit Ethernet is being deployed where needed
  40/100 Gigabit Ethernet is under development

## Slide 32: Wireless LANs
  802.11 architecture/protocol stack »
  802.11 physical layer »
  802.11 MAC »
  802.11 frames »

## Slide 33: 802.11 Architecture/Protocol Stack (1)
Wireless clients associate to a wired AP (Access Point)
  Called infrastructure mode; there is also ad-hoc mode with no AP, but that is rare.
Access Point
Client
To Network

## Slide 34: 802.11 Architecture/Protocol Stack (2)
MAC is used across different physical layers

## Slide 35: 802.11 physical layer
  NICs are compatible with multiple physical layers
    E.g., 802.11 a/b/g
Name | Technique | Max. Bit Rate
802.11b | Spread spectrum, 2.4 GHz | 11 Mbps
802.11g | OFDM, 2.4 GHz | 54 Mbps
802.11a | OFDM, 5 GHz | 54 Mbps
802.11n | OFDM with MIMO, 2.4/5 GHz | 600 Mbps

## Slide 36: 802.11 MAC (1)
  CSMA/CA inserts backoff slots to avoid collisions
  MAC uses ACKs/retransmissions for wireless errors

## Slide 37: 802.11 MAC (2)
Virtual channel sensing with the NAV and optional RTS/CTS (often not used) avoids hidden terminals

## Slide 38: 802.11 MAC (3)
  Different backoff slot times add quality of service
    Short intervals give preferred access, e.g., control, VoIP
  MAC has other mechanisms too, e.g., power save

## Slide 39: 802.11 Frames
  Frames vary depending on their type (Frame control)
  Data frames have 3 addresses to pass via APs

## Slide 40: Broadband Wireless
  802.16 Architecture / Protocol Stack »
  802.16 Physical Layer »
  802.16 MAC »
  802.16 Frames »

## Slide 41: 802.16 Architecture/Protocol Stack (1)
Wireless clients connect to a wired basestation (like 3G)

## Slide 42: 802.16 Architecture/Protocol Stack (2)
MAC is connection-oriented; IP is connectionless
  Convergence sublayer maps between the two

## Slide 43: 802.16 Physical Layer
Based on OFDM; base station gives mobiles bursts (subcarrier/time frame slots) for uplink and downlink

## Slide 44: 802.16 MAC
Connection-oriented with base station in control
  Clients request the bandwidth they need
Different kinds of service can be requested:
  Constant bit rate, e.g., uncompressed voice
  Real-time variable bit rate, e.g., video, Web
  Non-real-time variable bit rate, e.g., file download
  Best-effort for everything else

## Slide 45: 802.16 Frames
  Frames vary depending on their type
  Connection ID instead of source/dest addresses
(a) A generic frame. (b) A bandwidth request frame
(b)
(a)

## Slide 46: Bluetooth
  Bluetooth Architecture »
  Bluetooth Applications / Protocol »
  Bluetooth Radio / Link Layers »
  Bluetooth Frames »

## Slide 47: Bluetooth Architecture
Piconet master is connected to slave wireless devices
  Slaves may be asleep (parked) to save power
  Two piconets can be bridged into a scatternet

## Slide 48: Bluetooth Applications / Protocol Stack
Profiles give the set of protocols for a given application
  25 profiles, including headset, intercom, streaming audio, remote control, personal area network, …

## Slide 49: Bluetooth Radio / Link Layers
Radio layer
  Uses adaptive frequency hopping in 2.4 GHz band
Link layer
  TDM with timeslots for master and slaves
  Synchronous CO for periodic slots in each direction
  Asynchronous CL for packet-switched data
  Links undergo pairing (user confirms passkey/PIN) to authorize them before use

## Slide 50: Bluetooth Frames
Time is slotted; enhanced data rates send faster but for the same time; addresses are only 3 bits for 8 devices
(b)
(a)
(a)
(b)

## Slide 51: RFID
  Gen 2 Architecture »
  Gen 2 Physical Layer »
  Gen 2 Tag Identification Layer »
  Gen 2 Frames »

## Slide 52: Gen 2 Architecture
Reader signal powers tags; tags reply with backscatter

## Slide 53: Gen 2 Physical Layer
  Reader uses duration of on period to send 0/1
  Tag backscatters reader signal in pulses to send 0/1

## Slide 54: Gen 2 Tag Identification Layer
Reader sends query and sets slot structure
Tags reply (RN16) in a random slot; may collide
Reader asks one tag for its identifier (ACK)
Process continues until no tags are left

## Slide 55: Gen 2 Frames
  Reader frames vary depending on type (Command)
    Query shown below, has parameters and error detection
  Tag responses are simply data
    Reader sets timing and knows the expected format
Query message

## Slide 56: Data Link Layer Switching
  Uses of Bridges »
  Learning Bridges »
  Spanning Tree »
  Repeaters, hubs, bridges, .., routers, gateways »
  Virtual LANs »

## Slide 57: Uses of Bridges
Common setup is a building with centralized wiring
  Bridges (switches) are placed in or near wiring closets
This is a premises or structured wiring system as seen in an office

## Slide 58: Learning Bridges (1)
A bridge operates as a switched LAN (not a hub)
  Computers, bridges, and hubs connect to its ports

## Slide 59: Learning Bridges (2)
Backward learning algorithm picks the output port:
  Associates source address on frame with input port
  Frame with destination address sent to learned port
  Unlearned destinations are flooded (sent to all other ports)
Needs no configuration
  Table entries time-stamped
    Stale table entries dropped to allow changes
  Bandwidth efficient for two-way traffic

## Slide 60: Learning Bridges (3)
Bridges extend the Link layer:
  Use but don’t remove Ethernet header/addresses
  Do not inspect Network header

## Slide 61: Spanning Tree (1) – Problem
Bridge topologies with loops and only backward learning will cause frames to circulate for ever
  Need spanning tree support to solve problem

## Slide 62: Spanning Tree (2) – Algorithm
  Subset of forwarding ports for data is used to avoid loops
  Selected with the spanning tree distributed algorithm by Perlman
I think that I shall never see
A graph more lovely than a tree.
A tree whose crucial property
Is loop-free connectivity.
A tree which must be sure to span.
So packets can reach every LAN.
First the Root must be selected
By ID it is elected.
Least cost paths from Root are traced
In the tree these paths are placed.
A mesh is made by folks like me
Then bridges find a spanning tree.
– Radia Perlman, 1985.

## Slide 63: Spanning Tree (3) – Example
After the algorithm runs:
    B1 is the root, two dashed links are turned off
    B4 uses link to B2 (lower than B3 also at distance 1)
    B5 uses B3 (distance 1 versus B4 at distance 2)

## Slide 64: Repeaters, Hubs, Bridges, Switches, Routers, & Gateways
Devices are named according to the layer they process
  A bridge or LAN switch operates in the Link layer

## Slide 65: Virtual LANs (1)
VLANs (Virtual LANs) splits one physical LAN into multiple logical LANs to ease management tasks
  Ports are “colored” according to their VLAN

## Slide 66: Virtual LANs (2) – IEEE 802.1Q
Bridges need to be aware of VLANs to support them
  In 802.1Q, frames are tagged with their “color”
  Legacy switches with no tags are supported

## Slide 67: Virtual LANs (3) – IEEE 802.1Q
802.1Q frames carry a color tag (VLAN identifier)
  Length/Type value is 0x8100 for VLAN protocol

## Slide 68: End
Chapter 4